## Slide 1: Magnetic field safety
UCSB EH&S Radiation Safety Office

## Slide 2: Magnetic field safety
UCSB EH&S Radiation Safety Office
scope
This training applies to all users of devices and equipment designed to generate magnetic fields, both static and time varying.
Some common examples include:
MRI (magnetic resonance imaging)
NMR (Nuclear magnetic resonance)
Particle accelerators
Degaussers

## Slide 3: Magnetic field safety
UCSB EH&S Radiation Safety Office
Definitions & conversions
H Field: Magnetic field strength, measured in amps per meter (A/m)
B Field: Magnetic flux density. This quantity is considered the better measure of health hazards than the H field. The units are tesla (T) and gauss (G)
E Field: Electric field strength, measured in volts per meter (V/m)
_________________________________________________________________________
1 μT = 0.7958 A/m
1 A/m = 1.257 μT
1 T = 10,000 gauss = 1 weber/m2

## Slide 4: Magnetic field safety
UCSB EH&S Radiation Safety Office
Magnetic Field Characteristics
Magnetic fields:
  Are produced by electric currents
  Cannot be detected by natural senses
  Measured in units of tesla (T) or gauss (G)
    1 T = 10,000 G
  Decreases in strength with distance from the device
  Are usually continuously being produced by the device, even when not in operation

## Slide 5: Magnetic field safety
UCSB EH&S Radiation Safety Office
Health & Safety concerns
Physical effects: static and time varying fields
Magnetic fields can interfere with the operation of medical implants (e.g. pacemakers, etc.), resulting in serious injury or death
Magnetic fields can also exert forces on ferromagnetic medical implants (e.g. aneurysm clips, bone plates and screws, etc.), resulting in serious injury or death
Magnetic fields can also exert forces on ferromagnetic tools, jewelry and objects, creating dangerous projectiles that can result in serious injury or death, and can damage expensive equipment

## Slide 6: Magnetic field safety
UCSB EH&S Radiation Safety Office
Partial List of affected Implants (consult your physician if unsure about any implants)
Implanted cardiovascular defibrillator | Electronic implant or device | Ear implant
Magnetically-activated implant or device | Cardiac pacemaker | IV access port
Vascular access port and/or catheter | Spinal cord stimulator | Shunt
Artificial heart valve, coil, filter or stent | Internal electrodes or wires | Tissue expander
Neurostimulator and/or Biostimulator | Any type of prosthesis | Aneurysm clip(s)
Bone growth/bone fusion stimulator | Insulin or other infusion pump | Cardiac pacemaker
Artificial eye or eyelid spring | Heart valve prosthesis | Penile implant
Radiation (brachytherapy) seeds or implants | Artificial or prosthetic limb | Hearing aids
Surgical staples, clips, surgical mesh or metallic sutures | Intrauterine device (IUD), diaphragm or pessary | Wire mesh implant
Bone/joint pin, screw, nail, wire, plate, etc. | Vascular access port and/or catheter | Wig/hair implants
Dentures, false teeth, retainers, braces, partial plates and other metallic dental work | Any metallic fragment or foreign body | Implanted drug pump
Body piercing, tattoo or tattooed makeup | Joint replacement (hip, knee, etc.) | Other implants

## Slide 7: Magnetic field safety
UCSB EH&S Radiation Safety Office
Health & Safety concerns
Biological effects: static fields
Cancer?
  The ability of static fields to cause cancer and other biological effects is greatly disputed. There is currently no scientific consensus opinion on this issue. However, some conservative exposure limits are proposed based on the best available data.
Effects on the Heart
  Based on data from MRI usage, static fields may cause a small, reversible effect on electrocardiogram data. The cause is the interaction of moving blood and the field in the heart. The effect was minimal below about 2 T (20,000 G) and is not considered a concern.

## Slide 8: Magnetic field safety
UCSB EH&S Radiation Safety Office
Health & Safety concerns
Biological effects: time varying fields
Induced electrical current
  An electric current can be induced when a conductor (e.g. human body) is in a time varying field.
  Usually this is not a concern, but pacemaker users could be at risk. The induced currents may cause the pacemaker to incorrectly start pacing or even prevent pacing when it is actually needed.
Changes in the threshold for nerve and muscle action
  Can occur when current densities are at or above 100 mA/m2
  The magnetic field required to generate 100 mA/m2 is very large. (10T/sec or 100,000 G/sec)
Local Heating (MRI)
  Caused by the radiofrequency range time varying field
  Locally deposited extra heat can cause burns
  Low frequency fields generally do not contribute

## Slide 9: Magnetic field safety
UCSB EH&S Radiation Safety Office
Magnetic field exposure limits
Static fields
UCSB recognizes thresholds published by the American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Values (TLV) data
  ACGIH emphasizes that: “These values should be used as guides in the control of exposure to static magnetic fields and should not be regarded as fine lines between safe and dangerous levels.”
G – Gauss; a unit of magnetic field intensity, T – Tesla; magnetic field strength mT – millitesla | TWA – time weighted average
50,000 G (5T) | Extremity ceiling limit (no exposure allowed above this limit)
20,000 G (2T) | Extremity ceiling limit (no exposure allowed above this limit)
6000 G (600mT) | Allowed TWA for routine exposure (extremities) (8-hour TWA*)
600 G (60mT) | Allowed TWA for routine exposure (whole body) (8-hour TWA*)
30G (3.0mT) | Kinetic energy hazard from small ferrous objects
10G (1.0mT) | Damage to watches, credit cards, magnetic tape, and computer disks
5 G (0.5mT) | Highest allowed field for implanted cardiac pacemakers

## Slide 10: Magnetic field safety
UCSB EH&S Radiation Safety Office
Magnetic field exposure limits
Time Varying Fields (ACGIH)
General Public
  Exposures to 50/60 Hz for those with pacemakers should not exceed 0.1 mT (1 G). Other frequencies retain 0.5 mT (5G) limit.
Whole Body
  50/60 Hz: 0.5 mT (5 gauss) time-weighted average over 8 hours
  1 – 300 Hz: 60 mT/Hz
  300 Hz – 30 kHz: 0.2 mT
  > 30 kHz: contact EHS
Extremities
  50/60 Hz: 0.5 mT (5 gauss) time-weighted average over 8 hours
  1 – 300 Hz: 300 mT/Hz (arms and legs)
  600 mT/Hz (hands and feet)
  300 Hz – 30 kHz: 0.2 mT
  > 30 kHz: contact EHS

## Slide 11: Magnetic field safety
UCSB EH&S Radiation Safety Office
Safety Controls (1)
5 gauss Line
  It is generally accepted that magnetic fields below 5 gauss (0.5 mT) are not capable of causing adverse health effects (1 gauss for 50/60 Hz)
  Therefore, safety controls are utilized to prevent the exposure of individuals with medical implants to magnetic fields in excess of 5 gauss
  Similarly, safety controls are utilized to exclude ferromagnetic tools and objects from magnetic fields in excess of 5 gauss

## Slide 12: Magnetic field safety
UCSB EH&S Radiation Safety Office
Safety controls (2)
Engineering Safety Controls
  Should be first line of defense
  Generally more reliable and should be given priority
Administrative (Procedural) Safety Controls
  The second line of defense against magnetic field hazards
  Only when engineering controls are impractical or inadequate

## Slide 13: Magnetic field safety
UCSB EH&S Radiation Safety Office
Engineering Controls
Access Control – Prevents access to magnetic fields in excess of 5 gauss. Magnetic fields outside must be below 5 gauss
  Locked Room
    Best option if magnetic field producing device is located in a dedicated lab
    If this is not feasible or impractical, the use of safety stanchions is acceptable
Faraday Cage – Shields individuals from magnetic fields
  Typically consists of a closely spaced mesh made of conducting metal (e.g. copper)
  Typically installed in walls, windows, ceiling and flooring
Non-Magnetic Tools and Equipment
  A strong fridge/bar magnet can be used to confirm item is non-magnetic

## Slide 14: Magnetic field safety
UCSB EH&S Radiation Safety Office
Administrative Controls
Safety Signage – Posted in a conspicuous location at entrances to an area in excess of 5 gauss to warn them of the hazards
Safety Screening – Before entering an area in excess of 5 gauss, individuals must ensure they do not have any medical implants capable of being affected by magnetic fields, or ferromagnetic items (e.g. tools, keys, jewelry, equipment, etc.)
5 gauss Line – Typically a caution line on the floor that marks the area in excess of 5 gauss
Magnetic Field Safety Training – Required for everyone working in an area

## Slide 15: Magnetic field safety
UCSB EH&S Radiation Safety Office
Cryogenic safety
Cryogenic Safety
  Many magnetic field producing devices require the use of cryogenic fluids such as helium and/or nitrogen which presents additional safety concerns.
  When handling these materials remember to always use proper personal protective equipment (PPE).
    Face shield, safety glasses or goggles
    Cryogenic gloves
    Body protection

## Slide 16: Magnetic field safety
UCSB EH&S Radiation Safety Office
o2 displacement
Oxygen Displacement
  When vaporized into gas, all of these liquefied gases increase many hundreds of times in volume.
    Breathing in a pure inert gas environment for 5 to 10 seconds is sufficient to lose consciousness.
    Longer periods of time can cause asphyxiation and death.
  In some lab or space configurations, oxygen displacement is a serious concern, especially during a magnet quench.
    Always store liquefied gas in well ventilated areas.
    Oxygen monitoring may be required. Contact EH&S for assistance.

## Slide 17: Magnetic field safety
UCSB EH&S Radiation Safety Office
Worker Responsibilities
Performs a safety screening before entering an area in excess of 5 gauss
Promptly reports any actual or suspected injury to the supervisor
Informs the supervisor and the Radiation Safety Office of any safety concerns.

## Slide 18: Magnetic field safety
UCSB EH&S Radiation Safety Office
Supervisor responsibilities
Ensure that workers have completed the magnetic field safety training before giving access
Ensure that workers obtain medical care following an actual or suspected injury
Contact the Radiation Safety Office if:
  Changes have been made to the facility
  The magnetic field producing device is moved
  If a magnetic field producing device is acquired
  If an actual or suspected injury occurs

## Slide 19: Magnetic field safety
UCSB EH&S Radiation Safety Office
Radiation safety office
Magnetic Field Safety at UCSB is managed by the Radiation Safety Office
The Radiation Safety Office does the following:
  Performs hazard analysis
  Recommends and implements safety controls
  Provides safety training
  Performs safety inspections
  Performs accident investigation and implements corrective actions

## Slide 20: Magnetic field safety
UCSB EH&S Radiation Safety Office
Injury response
If an actual or suspected injury occurs:
  Do not move person unless further injury is likely.
  For emergencies, call 911 (9-911 if on-campus)
  Inform the Radiation Safety Office (x7255) as soon as possible.
  Submit a Employee First Report (EFR) form. See Worker’s Compensation Program Website or contact 805-893-3145 for more information.
  Submit a Employer Investigation (See EFR Tutorial)
  Do not use the magnetic field producing device until the Radiation Safety Office has evaluated the incident and corrective actions have been taken.

## Slide 21: Magnetic field safety
UCSB EH&S Radiation Safety Office
Near miss
OHSA defines a near miss as “an unplanned event that did not result in injury, illness or damage – but had the potential to do so.” A near miss is also referred to as a “close call” or “good catch.”
UCSB employees and students may use this form to report a near miss to EH&S.
EH&S will follow up to determine what corrective actions may be required to prevent a future recurrence.
Reports may be submitted anonymously if desired.
Employees are advised that it would be illegal for an employer to take any action against an employee in reprisal for exercising their rights to report safety issues.

## Slide 22: Magnetic field safety
UCSB EH&S Radiation Safety Office
quiz
A misplaced or unrestrained metallic object inside of a strong magnetic field can act as a projectile moving exponentially faster towards a magnet.
a. True
b. False
2. People with implanted medical devices, such as a pacemaker, should NOT cross the 5 gauss line because it could interfere with the device’s operation.
a. True
b. False

## Slide 23: Magnetic field safety
UCSB EH&S Radiation Safety Office
quiz
3. Locking the lab door to prevent access to magnetic fields in excess of 5 Gauss is considered which type of safety control?
a. Administrative Control
b. Engineering Control
4. Requiring all individuals, before entering an area in excess of 5 Gauss, to ensure they are free of any medical implants capable of being affected by magnetic fields, or ferromagnetic items (e.g. tools, keys, jewelry, equipment, etc.) is an example of which type of safety control?
a. Administrative Control
b. Engineering Control

## Slide 24: Magnetic field safety
UCSB EH&S Radiation Safety Office
quiz
5. When should the Radiation Safety Office be contacted?
a. When a magnetic field producing device is acquired
b. Changes have been made to the facility or magnetic field producing device is moved
c. An actual or suspected injury occurs
d. All the above
6. What additional hazard is associated with time-varying magnetic fields rather than static fields?
a. Risk of blindness
b. Damage to credit cards
c. Induced electrical currents
d. Cancer

## Slide 25: Magnetic field safety
UCSB EH&S Radiation Safety Office
quiz
7. What is the highest STATIC magnetic field exposure allowable for implanted cardiac pacemakers and the general public?
a. 1 gauss (0.1 mT)
b. 5 gauss (0.5 mT)
c. 10 gauss (1.0 mT)
d. 50 gauss (5.0 mT)
8. What is the highest 50/60 Hz magnetic field exposure allowable for implanted cardiac pacemakers and the general public?
a. 1 gauss (0.1 mT)
b. 5 gauss (0.5 mT)
c. 10 gauss (1.0 mT)
d. 50 gauss (5.0 mT)

## Slide 26: Magnetic field safety
UCSB EH&S Radiation Safety Office
quiz
9. When handling cryogenic materials which items of proper personal protective equipment (PPE) should be worn?
    Face shield, safety glasses or goggles.
    Cryogenic gloves.
    Body protection.
    All of the above.
10. When using liquefied gases, what can be done to prevent O2 displacement?
a. Use and store materials in well ventilated area.
b. Always have an emergency exit.
c. Install oxygen monitors.
d. Both a and c.